## Slide 1: Possible Damping Ring Timing
Kazuro Furukawa
Injector Linac, KEK
<kazuro.furukawa@kek.jp>
Some info at <http://www-linac.kek.jp/cont/epics/event/>
Conference papers at <http://www-linac.kek.jp/linac/>

## Slide 2: Bucket selection in Phase-2 with DR
Without DR, simply wait up to 5120 x 96 ns ~ 490 μs
  96 ns : highest common frequency between linac – ring
With DR, in order to select arbitrary bucket in MR, have to wait up to ~4.5 ms, even if a bucket in DR was carefully selected
  Power supply can wait only 2 ms, one of only 2798 buckets in 5120 buckets can be selected, may have to change LLRF condition at latter half of linac every pulse
  Can be a big challenge in LLRF precision
ARC
e+ Target
e+ BT (3.5GeV, 0.6nC)
e− Gun
KEKB
Primary e– (3.5GeV, 10nC)
ARC
e+ Target
e+ BT (KEKB: 4GeV, 4nC)
e− Gun
SuperKEKB
Primary e– (3.5GeV, 10nC)
e+ DR (1.1 GeV, 4nC)
96ns
>100ns
>100ns
96ns
DR timing

## Slide 3: Memo from Oct.6.2016
32k 周 14ms 分記録
読み出しは 12 枚で 0.5秒
2ns または 4ns step
Bunch 同期信号、入射 Kicker を打ってから Revolution で Timing を打ち続ける
  20% の Duty 比、TTL
  入射 Kicker が打ったらそれに同期する、つまり 2 pulse 溜めたときには、最初の pulse は無視
    ???
Start 信号、入射 Kicker から、(NIM)/TTL
さらに Revolution を一ヶ所 2 種類
  一つは MR RF から作った DR Revolution と DR RF から作った DR Revolution の 2 つ
  入出射 Kicker / BPM EVR で一方の Revolution を作れば良い
  15 slot VME64x x2箱
Dispersion 測定のために 509 MHz を振る
  +/- 50kHz
そのため、Linac 同期の 509 MHz/Revolution は使えない
おそらく Main event system とは切り離した
  Event system または新規開発信号分配 System が必要
Dispersion 測定後に出射 Kicker を同期できるか不明
  その場合はその独立 Event System 側が出射 Kicker を打つ
  Kicker 側は 親 Event system と独立 Event system の双方から Kicker signal を受ければ良い

## Slide 4: Distributed bus and multiplexed counters
The distributed bus allows transmission of eight simultaneous signals with the event clock rate time resolution (10 ns at 100 MHz event clock rate). The source for distributed bus signals may come from an external source or the signals may be generated with programmable multiplexed counters (MXC) inside the event generator. The distributed bus signals may be programmed to be available as hardware outputs on the event receiver.

## Slide 5: MXC and Sequencer
The end sequence code 0x7f resets the sequencer RAM table address and timestamp register and depending on configuration bits, disables the sequencer (single sequence, SQxSNG=1) or restarts the sequence either immediately (recycle sequence, SQxREC=1) or waits for a new trigger (SQxREC=0).

## Slide 7: Pulse-to-pulse modulation
ARC
e– (2.5GeV, 0.2nC)
e− Gun
ARC
e+ Target
e+ (4GeV, 4nC)
e− Gun
PF Injection
SuperKEKB-LER Injection
e– (3.5GeV, 10nC)
ARC
e– (7GeV, 5nC)
e− Gun
SuperKEKB-HER Injection
ARC
e– (6.5GeV, 5nC)
e− Gun
PF-AR Injection
Damping ring
Event-based Control System
Every 20 ms
F.B
F.B
F.B
F.B
F.B
F.B
F.B
F.B
Four PPM virtual accelerators for SuperKEKB project Based on Dual-tier controls with EPICS and event-system Independent parameter sets for each VA (20ms) >200 parameters for equipment controls many more for beam controls maybe with additional PPM VA of stealth beam for measurement