## Slide 1: Injector Linac Energy Margin Answers to injector questions at Moday talk
Kazuro Furukawa
Injector Linac, KEK

## Slide 2: Mission of Electron/positron Injector in SuperKEKB
  For 40-times higher luminosity in SuperKEKB collider
  Low emittance & low energy spread injection beam with 4-5 times more beam current
    New high-current photo-cathode RF gun developments
    New positron capture section
    Damping ring construction
    Optimized beam optics and correction
    Precise beam orbit control with long-baseline alignment
    Simultaneous top-up injection to DR/HER/LER/PF/PFAR
  Balanced injection for the both photon science and elementary particle physics experiments
Linac Mission in FY2016-FY2017
The single injector would behave as multiple injectors to multiple storage rings by the concept of virtual accelerator
1
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: Linac Energy Margin in Phase II
Construction budget is so tight that no backups are prepared for many components (common understanding)
As the acceleration units are indispensable, for Y(4s) in Phase-II at least a single backup/stand-by unit (~150 MeV) is prepared for each of three linac sections
  Sections: J-Arc (1.5 GeV), SY2-DR (1.1 GeV e+), SY3-Linac-end (7 GeV e– / 4 GeV e+)
  51 units for acceleration and 9 units for beam manipulation
However, Y(6s) was out of consideration for Phase-II
  It may be possible to operate for Y(6s) without backups (J-Arc 1.7 GeV)
  Need to reach an understanding with PF / PF-AR for possible interference
  Before that, we surely have to establish low emittance beam injection
There are many failure modes of units, typical ones are;
  High power klystrons [a few times a year]
    Two and a half days to replace a klystron
  High power klystron pulse modulators [once or twice a year]
    From a shift to several days depending on the failures
  Fatal damage in accelerator structures [once in a few years]
    Several days to replace a structure
      Frequency of the appearance has been increasing
Kamitani et al
In Phase II Commissioning

## Slide 4: Linac Energy Margin in Phase III
Unit #13 will be added in Phase-III (+150 MeV)
  Securing well-performed accelerator structures in #44, the unit will be converted to high-gradient by adding another klystron (+70 MeV)
On failures, the J-Arc energy may be changed to help other sections depending on the failure mode
  If really relevant, DR energy may be changed to help e+ (?)
In the long run, degraded accelerating structures should be refurbished
Bunch Compression
A
B
C
1
2
3
4
5
SuperKEKB PF/AR Injector
HER
7.0 GeV
5nC x 2
20 um
LER
4.0 GeV
4nC x 2
Primary electron
2.9 GeV, 10nC x 2
1.1 GeV
e+ damping ring
Energy Compression
Bunch Compression
PF
2.5 GeV
0.2nC x 1
New RF gun 5 nC
Thermionic gun 10 nC
New Positron Capture Section
PF-AR
6.5 GeV
0.2nC x 1
J-arc
1.5 GeV
Energy Compression
Slow Positron
Kamitani et al
In Phase III Commissioning

## Slide 5: Why Smaller Margin while dropping Energy 8 GeV  7 GeV
No backup/stand-by before J-Arc in KEKB operation
Optimized for SuperKEKB ring injection reliability with larger beam currents and smaller emittance
A unit was removed to make a room for DR BT
Positron deceleration capturing
Lower acceleration in large aperture structures in the positron capture section
An unit before J-Arc was converted into a stand-by for availability
C-band structures were converted into S-band to help emittance preservation
Degraded accelerating structures after 35 years of operation
Larger beam current with larger beam loading
Kamitani et al

## Slide 6: Development of Photo-cathode RF Gun
Succeeded in injection during SuperKEKB Phase 1 commissioning for 11 days
Employs Yb-doped-fiber and Yb:YAG laser, Ir5Ce cathode, quasi travelling wave side-coupled cavity
Need stability improvements
Beam instrumentation improvement and comparison with simulation codes underway
Secondary RF gun is being constructed as a backup
Incorporate suggestions by review committee for availability
Beam orbit measurement
Bunch width
Thermionic gun
Primary RF gun
New secondary RF gun
One of Key Component: Photo Cathode RF Gun
Ir5Ce Cathode
Quasi traveling wave side couple cavity

## Slide 7: Development and installation of pulsed magnets
  Pulsed magnet power supplies were postponed to 2017 because of resource availability
  30 quads, 36 steerings, 2 bends, 13 girders will be fabricated and installed in 2017
  Quads with aggressive design at 1 mH, 330 A, 340 V, 1 ms with energy recovery up to 75%
  Essential for SuperKEKB low emittance injection and simultaneous injections
  4+1 ring injections with virtual accelerator concept
  Risks against schedule and possible backup operation procedure are investigated
    Long term tests at a stand
    Satisfies specifications
    Some more control capability
    Synchronous operation in 2017
    Beam test with two quads
    Successful 25 Hz beam switches
    Basic features are completed
    Event timing synchronization needed
    Girders are tested as well
    In-house drawings to save rsc.
    0.1mm alignment precision
    Ready for Phase-3 upgrade
One of Key Component: Pulsed Magnets

## Slide 8: Possible Rescheduling
Under limited resources rescheduling of fabrication, purchase, tests, installation, commissioning is planned
Because of construction concentration in JFY2017, 5-month shutdown of injector is planned
  for KEKB it could allocate 9-month shutdown in 1997, synchronizing with light source upgrade