## Slide 1: Injector Linac
  Kazuro Furukawa
  for Injector Linac Groups
  Many slides from M. Satoh and N. Iida
  <http://www-linac.kek.jp/linac/>
  < kazuro.furukawa @ kek.jp >
< kazuro.furukawa @ kek.jp >

## Slide 2: Contents
Injector status
  Overview
  Beam sources
  Accelerator components
    Structures, pulsed magnet, monitors, operation tools
  Injection management
    Anomalous injection beam
  Beam controls
    Especially positron beam emittance improvements
  Background spikes
    Mystery
  Summary

## Slide 3
Overview

## Slide 4: Fire Recovery
Fire at acc. structure assembly room on Apr.3
  Southern part of the injector was much damaged as well as the assembly room
Interim injector recovery by Apr.26
Full injector recovery during summer shutdown
The assembly room cleaned up
  Restoration in April
  S-band structure tests and RF conditioning soon
Scaffold to clean up walls and ceiling
at acc. structure assembly room

## Slide 5: Mission of Electron/positron Injector in SuperKEKB
  Low emittance & low energy spread injection beams with 4 times higher beam current
    New high-current photo-cathode RF gun
    New positron capture section
    Positron damping ring injection/extraction
    Optimized beam optics and correction
    Precise beam orbit control with long-baseline alignment
    Simultaneous top-up injection to DR/HER/LER/PF/PFAR
  Balanced injection for the both photon science and elementary particle physics experiments
Injector Linac Mission
The single injector would behave as multiple injectors to multiple storage rings by the concept of virtual accelerator
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 6: Linac Beam Parameters at KEKB/SuperKEKB
Linac Beam Property Requirements
Limited improvements for operational electricity budget
Stage | KEKB (final) |  | Phase-I |  | Phase-II |  | Phase-III (interim) |  | Phase-III (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1.0 A | 1.0 A | – | – | 1.8 A | 1.3 A | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | – | – | 6 | 6
 | primary e- 10 |  | primary e- 8 | 1 | 0.5 | 1 | 2 | 2 | primary e- 10 | 4
Bunch charge (nC) | → 1 | 1 | → 0.4 |  |  |  |  |  | → 4 | 
Norm. Emittance | 1400 | 310 | 1000 | 130 | 200/40 | 150 | 150/30 | 100/40 | 100/15 | 40/20
(gbe) (mrad) |  |  |  |  | (Hor./Ver.) |  | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.)
Energy spread | 0.13% | 0.13% | 0.50% | 0.50% | 0.16% | 0.10% | 0.16% | 0.10% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Partially |  | 4+1 rings (LER, HER, DR, PF, PF-AR) |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 

## Slide 7: Simultaneous 4 + 1 Ring Top-up Injection
Realized for the first time
    SuperKEKB HER 7 GeV e–
    SuperKEKB DR and LER 4 GeV e+
    Photon Factory 2.5 GeV e–
    PF-AR 5.0 / 6.5 GeV e–
  4 beams are modulated at 20-ms PPM (pulse-to-pulse modulation)
  More than 200 pulsed devices were constructed for SuperKEKB, as well as many beam and RF monitors
  Injection noise (background) were well studied by Belle II and MDI group
HER
LER
PF
PF-AR

## Slide 8: Simultaneous Top-up Injections
SuperKEKB integrated luminosity improvement
17.5 /pb in 5.15 hr
(5 fills)
on May.6
41.6 /pb in 5.15 hr
(top-up)
on May.16
237% improvement

## Slide 9
Beam Sources

## Slide 10
Pulse to pulse switching: rf e- gun/thermionic e- gun
Thermionic DC e- gun (GU_AT)
w/ 2 subharmonic bunchers and 2 bunchers
・e+ production e-: 10 nC (for LER injection)
・PF injection: 0.3 nC
・PF-AR injection: 0.3 nC
RF e- gun
（GR_A1 for HER injection）
Pulsed bend rep. up to 25 Hz (LER + PF + PF-AR)
(magnet coil and chamber heating issue)
It will be replaced by new one in summer shutdown 2020 for full 50 Hz operation.
Notes: 入射部では24度垂直偏向パルスベンドを用いて，熱電子銃，RF電子銃を切り替えて運転している．
熱電子銃は，陽電子生成用10 nC電子ビーム，PF,PF-AR入射用 0.3 nCビームを生成している．
RF電子銃は，HER入射用低エミッタンス電子ビームを生成している．（レーザー両打ち，IrCeカソード）電子銃からは，最大2～3 nC出る．

## Slide 11: Development of Photo-cathode RF Gun
Successfully deployed for injection into SuperKEKB HER
Employs Yb-doped-fiber and Nd/Yb:YAG laser, IrCe cathode, QTWSC or cut disk cavities
Stability improving
Beam instrumentation improvements and comparison with simulation codes
Secondary RF gun was constructed as a backup (under tuning)
Incorporate suggestions by review committee for availability
Beam orbit measurement
Bunch length
Thermionic gun
Primary RF gun
Secondary RF gun
One of Key Component: Photo Cathode RF Gun
IrCe Cathode
Electron Guns
Cut disk cavity
M.Yoshida et al.
Quasi traveling wave side couple cavity

## Slide 12: RF e- gun
M. Yoshida, SuperKEKB review, Mar. 14th, 2018
Low emittance
RF gun
Photocathode
(metal composite: IrCe)
QTW RF gun or operation (0 deg. Line)
CDS RF gun
for backup (90 deg. Line)
e- source

## Slide 13: Hybrid laser system for rf gun
Optics layout in the tunnel
1st laser
2nd laser
1st + 2nd laser line:
laser line:
e- beam bunch length
10.93 ps (FWHM) at A1 streak camera
(‘19/11/20)
UV laser beam profile
UV laser beam profile
Three Oscillators (two of them are backup)
Yb doped fiber and Neodymium (Nd) doped laser crystal
R. Zhan, SuperKEKB review, 2019
e- source

## Slide 14: HER injection beam (RF e- gun) status
HER injection has been done with only RF gun since the beginning of Phase III (Mar. 11th, 2019)
Laser system has no significant fault
In summer shutdown 2019, photocathode (Ir7Ce2) was replaced by new one (Ir2Ce) aiming at better quantum efficiency (Qe)
  Discharge, frequent VSWR, gradual decrease of bunch charge
In this winter shutdown,
  After applying heat and laser cleaning of cathode, bunch charge was not stable.
  Finally, photocathode was replaced by previous one (Ir7Ce2) toward next run. Now, under rf conditioning.

## Slide 15: Qe of photocathode (Ir7Ce2, Ir2Ce)
M. Yoshida
e- source
15

## Slide 16
Ir7Ce2
2019
e- source
16

## Slide 17
discharge
discharge
VSWR
VSWR
VSWR
VSWR
VSWR
Ir2Ce
2019
e- source

## Slide 18
2020
e- source
One day
Ir7Ce2

## Slide 19: e+ source setup 1
Positron target and capture section
Y. Enomoto, SuperKEKB review, 2019
W target + flux concentrator (FC)
DC solenoid
Large aperture S-band acc. Structures (x10)
e+ source

## Slide 20: e+ source setup 2
target
BC (bridge coil)
FC(flux concentrator) head
LAS (large aperture S-band)
solenoid
FC head + BC + target = FC assembly
Y. Enomoto, SuperKEKB review, 2019
e+ source

## Slide 21: Positron generation for SuperKEKB
New positron capture section after target with Flux concentrator (FC) and large-aperture S-band structure (LAS)
Satellite bunch (beam loss) elimination with velocity bunching
Pinhole (2mm) for passing low-emittance electrons beside target (3.5mm)
Matching the beam optics for the damping ring injection
Flux
Concentrator
e+
4 nC injection e-
10 nC
primary e-
bridge coils
target
beam
hole
pulsed ST
DC quad
pulsed quad
top view
spoiler
solenoid
LAS Accel.
structure
positron
production
Target
Flux
Concentrator
Bridge
Coils
primary
e- beam
e+ beam
Positron Enhancement
Y.Enomoto et al.

## Slide 22
Primary
e- beam
e+ beam
e+ beam history in 2019
e+ source
2019
22

## Slide 23: After large discharge…
After large discharge
Slit gap got narrow.
Not possible to apply high voltage unless the gap will be expanded.
Y. Enomoto, SuperKEKB review, 2019
e+ source

## Slide 24: LER injection beam status
Bunch charge
  Stable and enough bunch charge in this stage
  Primary e-: 11 nC (from gun), 9 nC (on W target), e+ : 1.2 nC (linac end), 0.8 nC (BT)
Flux concentrator (FC)
  Previous FC was damaged by large discharge during PhaseII. It was removed in Sept. 2018.
  Current FC was installed in Jan. 2019.
  2 ～ 3 kA operation current (design 12 kA) for stable operation. no significant fault.
  New FC made of Cu-alloy (NC50: Cu-Si-Ni) has been tested w/o fault (～ 12 kA).
  New FC will be installed in summer shutdown of 2020 for aiming at design operation current.
Requirements for material of the FC head are
Good brazing characteristic
High yield strength even after brazing
High electric and thermal conductivity
e+ source

## Slide 25
Accelerator Components

## Slide 26: Accelerator Structure
Approx. 230 accelerator structures employed
Many aged (40 years-old) structures are degraded
  Risk of 7 GeV / 4 GeV acceleration for Y(4S)
  Cannot reach Y(6S)
As a 4-5 year plan, structures are being fabricated since the last year
First tests will be performed at the assembly room
Possibly, a couple of structures would be installed during summer

## Slide 27: Pulsed magnet system
Pulsed quads (x 28) (w/ ceramic duct) and steering (x 36) were installed at Sector3 to Sector5 in 2017 (on movable girder).
Pulsed bend, additional quad and steering were installed in 2018 summer and winter shutdown.
PXIe based control system (Windows 8.1, LabVIEW, EPICS) have worked fine w/o any serious trouble.
Power supply stability: 0.01% (24 hours)
Pulsed magnet
BPM
Movable girder for pulsed magnet
(remote controllable, 10 mm step)
Subsystems

## Slide 28: Movable girder for accelerating structure
Six movable girders have been installed in Sector3 (in summer shutdown of 2019).
  Four 2-m-long accelerating structures are mounted on one girder.
It could help to suppress emittance growth due to misalignment.
subsystems

## Slide 29: Monitors (1)
Beam position monitor (x 103)
  Four strip line electrodes (x 97)
    Measurement precision ~ 10 mm
  Eight strip line electrodes (x 6) (J-ARC, LTR x2, PF BT, HER BT, LER BT)
Profile monitor (x 104)
  Al2O3/CrO3 (AF995R, Demarquest Co.). (t: 1 mm, 0.1 mm), YAG:Ce (t: 0.1 mm)
Wire scanner (WS) (x 6)
  SectorA, B, C, 2, 3, 5
Streak camera (ST) (x 2)
  SectorA, C, 3
RF monitors for klystron, SLED, acc. structure
WS
WS
WS
WS
WS
ST
ST
ST
WS

## Slide 30: Monitors (2)
SR monitor was installed and tested in early stage of KEKB era (J-ARC and ECS at SY3). Then, they have been obsoleted. SR monitor at J-ARC has been renovated in summer shutdown of 2019.
Nondestructive beam profile monitor w/ triggered camera, and it could be utilized for energy spread feedback (together w/ 8 electrodes BPM).
Additional high resolution profile monitors: C2 (OTR), 58 (YAG)
Background measurement and calibration
Fitting results
SR monitor
8 electrodes BPM
subsystems

## Slide 31
Injection Management

## Slide 32: Injection BG tuning
+ Injection beam
Emittance
Orbit
Charge
Energy
Energy spread
Bunching
Laser
…
+ Injection tuning
Septum angle
Vertical angle
Energy
Injection phase
kicker height
…
+ Ring condition
  Optics correction
  (beta, X-Y coupling, dispersion)
  Tune
  iBumpFB target
  IP Knobs
  Collimator
  Luminosity
  …
+ Stability
No drift
No jitter
No
BG

## Slide 33: Injection efficiency and background
Injection tuning for squeezing by*
  Open collimators in the MR
  Squeeze by* -> Optics correction
  Injection tuning using Turn-by-turn BPMs
  Close collimators in the MR
 | LER | HER
Injection efficiency | ・The emittance and energy spread of the injection beam are now good enough for by*=1.0mm. | Depends on the vertical emittance and the energy spread of the injection beam
Background | ・Mainly comes from stored beam caused by vacuum condition. ・Low enough from injection usually. ・”Spike” and “Duration of injection BG” are most serious problems. | Mainly comes during Injection. Stability of e- beam should be resolved.

## Slide 34
by*=1.0mm
by*=1.2mm
The injection efficiency gradually increased.
Phase3.2
2019c(Autumn)
Injection efficiency and background
The background decreased.
unstable !
HER
ZOOM
Total current
HER, LER
Inj. eff. (HER)
Charge for HER
VXD-BW signal
Inj. eff. (LER)
Charge for HER
VXD-FW signal
Belle II
Diamond signal

## Slide 35
gey=144±24mm: 40%
gey=105±14mm: 55%
gey=83±23mm: 75%
gey=66±13mm: 100%
by*=1.0mm
The injection efficiency increased as emittance decreased by tuning day by day.
These efficiencies are calculated at the low current beam in the HER.
→ The effect of Touschek lifetime can be neglected.
Injection efficiency and background
Phase3.2
2019c(Autumn)
Energy spread became better

## Slide 36: Vertical emittance vs. HER Injection efficiency
Y. Ohnishi
Injection efficiency and background

## Slide 37
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
Y. Ohnishi
・LER
(28/Jun/2019)
(6/Nov/2019)
gex
[mm]
gey
[mm]
Reducing emittance is in time for by*=1mm

## Slide 38: When the vertical emittance was improved
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
6.Nov.2019 3:17
6.Nov.2019 18:50
BG due to injection became smaller.
Signals from Loss monitors in the LER
Injection efficiency and background
BGs from Vertex detectors
gex
[mm]
gey
[mm]
LER

## Slide 39
Beam Controls

## Slide 40: Feedback loops
Energy feedback (J-ARC, LTR, ECS, BT) loops work fine.
  Energy stability at BT line < 0.025%
Orbit feedback at some locations.
  Large drift (～ 1 mm) can be corrected
  within ~ 0.1 mm w/ feedback.
Energy @ BT
Orbit FB
Energy FB

## Slide 41: 2. Improvements of emittance growth
Residual dispersion
  Dispersion correction
  Residual dispersion at the acceleration for compression system
Abnormal skew magnetic field from bends
Emittance growth caused by jitters
Other sources
  Wake field in the LINAC
  Radiation excitation in the e- BT line

## Slide 42: Residual Dispersion Function Correction
Design
Before
After
Measured
Measured
Dispersion correction
Large residual dispersion function was generated at the 180-degree J–ARC, that caused beam instability.
Dispersion correction by tuning the magnetic field of quadrupole magnets made residual dispersion function small enough.
Y. Seimiya et al.

## Slide 43
1nC
Linac end:
28 μm
7 μm
Linac end:
1.8 μm
0.9 μm
J-ARC e+ target
J-ARC e+ target
Before dispersion correction
After dispersion correction
First figure shows the standard deviation of beam position. Second figure shows emittance growth induced by beam jitter.
Beam phase space jitter is reduced by dispersion correction.
Small emittance growth still occurred from after the target after the correction.
We should understand the source of the beam jitter to prepare for the high charged beam and for accidental jitter source which may occur at upstream.
Phase Space Jitter Reduction

## Slide 44: Beam emittance example (~1 nC) w/ multiple wire scanners
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
e+: ex/ey ～100/6 mm
e-: ex,y ～20 mm
e-: ex,y ～ 50～80 mm
e+: ex/ey ～100/2 mm
e-: ex/ey 40/20 mm
e+: ex/ey 100/15 mm
BT
#1 straight
Final target
e-: ex,y ～ 50～80 mm
e-: ex,y ～10~20 mm
e- emittance growth
e+: ex,y ～ 2500 mm (before DR)
Emittance
e-: ex/ey 100/40 mm
e+: ex/ey 180/30 mm
Interim target
Notes: 1 nCでのエミッタンス測定の典型的な例（4台のワイヤースキャナで測定）
Phase3の最終目標は，4 nCで中央下にある値．
1nCであるが，陽電子は，概ね最終目標エミッタンスを満たしている．
電子も1nCであるが，入射器内（5セクタ）では水平方向は50 um程度の場合もある．C～5セクタでのエミッタンス増大は，アライメントの改善と加速管架台ムーバーの導入で改善を図る予定である．
Phase2の時には，BTでエミッタンス増大が見られる（入射器5セクタの2～3倍のエミッタンスになる．100 um が300 um以上になる）問題があったが，BTワイヤスキャナのワイヤ径を200 umから60 umに変更し，データ収集系をCAMACから入射器と同じVMEベースのものに変更したところ，そのような増大が見られなくなった．（詳しい原因は不明ですが，測定系に問題があったと思われます．）

## Slide 45: Layout of LINAC, BT, Injection to MR
LER
HER
Damping Ring (DR)
for positron
Sector2
Sector3
Sector4
Sector5
Sector1
SectorA
SectorB
SectorC
Jarc
LINAC
Beam Transport line (BT)
e- : RF Gun
e+ target
Injection Points
BT1
e- beam directly injects into HER:
The injeciton BG is directly affected by the condition of RF-gun LINAC and BT.
e+ beam injects into LER via DR:
The injection BG is not affected very much by the condition upstream the DR.
primary e- for e+: Therminic Gun
BT1
Arc0
Arc1
BT2
Arc2-3
Arc4
green: Emittance measured with wire scanners
ECS: Energy Compression System
ECS
BCS
ECS
for e+
Notes: The contents of my talk is like these.
First, let me talk about the DR complex shortly.

## Slide 46: Layout of LINAC, BT, Injection to MR
LER
HER
Damping Ring (DR)
for positron
Sector2
Sector3
Sector4
Sector5
Sector1
SectorA
SectorB
SectorC
Jarc
LINAC
Beam Transport line (BT)
e- : RF Gun
e+ target
Injection
Points
HER:
VXD(Diamond) BW135
LER:
VXD(Diamond) FW135
Belle2
LINAC
Diamond detectors at VXD in Phase3
Most sensitive to the BG on Belle2.
e- beam directly injects into HER
e+ beam injects into LER via DR.
MR
Many loss monitors are around the MR.
The signals from the Diamonds and the loss monitors are carefully monitored to keep the BG low.
Some aborts are avoided by stopping injection when the signals are high.
primary e- for e+: Therminic Gun
Notes: The contents of my talk is like these.
First, let me talk about the DR complex shortly.

## Slide 47
Measured Emittance
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
e+ beam (Phase3.2(6.Nov.2019))
DR → Sector 3、
BT1 → BT2、
Emittances increase
→Need study
Phase3.3 | e+ | e-
gex [mm] | 150 | 100
gey [mm] | 30 | 40
sd [%] | 0.16(1s) | 0.1(1s)
e- beam (Phase3.2(4.Dec.2019))
B C ３ 5 BT1 BT2
B C ３ 5 BT1 BT2
C→Sector 3、
BT1→BT2、
Emittances increase
→Need study
gex
[mm]
gey
[mm]
gex
[mm]
gey
[mm]

## Slide 48: A) Residual dispersion
Dispersion correction
Before
After
Measured
Measured
Dispersion
correction
RMS Dhx = 0.43 m
gbex = 187 ± 27 mm
RMS Dhx = 0.02 m
gbex = 140 ± 33 mm
Δgbex = -47 mm
m
m
Thermionic gun
Design
J-ARC
m
(Emittance at the end of LINAC)
Y. Seimiya
for Example,
Improvements of emittance growth
Large residual dispersion had been observed at the Jarc before dispersion correction.
By tuning the strength of quadrupole magnets, residual dispersion became small.

## Slide 49: A) Residual Dispersion in the BT line
BT for e+
BT for e-
Dispersion function correction
The dispersion functions have been corrected for each BT ARC one by one.
Non-negligible residual dispersion is still observed
Straight line
(BT2)
Straight line
(BT2)
Straight line
(BT1)
Straight line
(BT1)
Improvements of emittance growth
Y. Seimiya

## Slide 50
Residual dispersion at the acceleration structure for a compression system
Improvements of emittance growth
Simulation result:
M. Kikuchi
Measured dispersion from ECS at the end of LINAC.
The dispersion is leak at the ECS cavity.
When the beam with finite dispersion function is accelerated by RF cavity, hd converts to betatron oscillation and causes emittance growth.
If the cavity has non-zero dispersion, a beam, gaining its energy depending on z, has net growth in the projected-emittance.
This is an analogue of the synchro-beta excitation at the cavity with non-zero dispersion in the ring.
ECS: Chicane+Acc

## Slide 51
T. Mori
BL along the horizontal direction
The bending magnets used in ECS/SY3 have quadrupole components.
  The beam feels B’ field passing through the design orbit in the bends, which makes dispersion leakage.
By moving the bends about 10mm, the beam pass the area of small B’.
~10 mm
This can explain the measured dispersion leak
  Improvements of emittance growth
Residual dispersion at the acceleration structure for a compression system (cont’d)
Magnetic field measurement
design orbit
-10mm
T. Kamitani, H. Kakihara, T. Oogoe
Bends were moved during sumer

## Slide 52
DIfference from design dispersion
ECS
ηx = 0.50 m @Acc.
ECS
ηx = 0.15 m @Acc.
Y. Seimiya
DR 3 5 BT1 BT2
LERの要求値
DR 3 5 BT1 BT2
1nC
The horizontal dispersion has been improved by moving ECS bends.
Still a large vertical emittance remained
Improvements of emittance growth
gex
[mm]
gey
[mm]

## Slide 53: 2. Improvements of emittance growth
Residual dispersion
  Dispersion correction
  Residual dispersion at the acceleration for compression system
Abnormal skew magnetic field from bends
Emittance growth caused by jitters
Other sources
  Wake field in the LINAC
  Radiation excitation in the e- BT line

## Slide 54: B) Abnormal skew magnetic field from bends
BT1
BT2
LINAC
LER
BTpositron
３rd Arc
e+
e+
Y. Seimiya
Dhy
Dhx
hy
hx
dispersions
(Measured-Design)
dispersions
(Measured)
Slope1
Slope2
Improvements of emittance growth

## Slide 55: Simulation
M. Kikuchi
Measured vertical dispersion before SkewQ
Calculated vertical dispersion by the skew quads which are installed.
Good agreement !
It is considered that the vertical dispersion could be corrected with the skew quads with permanent magnets.
e+ beam
Improvements of emittance growth
Since the energy of the e+ beam increased to 4 GeV from 3.5GeV of the old KEKB, the gap of bend narrowed asymmetry, which created an abnormal skew component in the bend.
However, this can only explain about one third of the measured skew quad component of the beam.
Anyway, try to correct.
~1 kgauss

## Slide 56
2. Improvements of emittance growth

## Slide 57
11 of 16 Skew Quads with permanent magnets were installed.
Improvements of emittance growth

## Slide 58: Measured Dispersion
① Before installation of skew quads
② After installation of skew quads
Y. Seimiya
Improvements of emittance growth
DR 3 5 BT1 BT2
DR 3 5 BT1 BT2
Remaining SkewQuads will further improve the vertical emittance.
gex
[mm]
gey
[mm]

## Slide 59: 2. Improvements of emittance growth
Residual dispersion
  Dispersion correction
  Residual dispersion at the acceleration for compression system
Abnormal skew magnetic field from bends
Emittance growth caused by jitters
  Jitter emittance from energy jitter
  Jitter from hardware components
Other sources
  Wake field in the LINAC
  Radiation excitation in the e- BT line

## Slide 60: C) Emittance growth caused by Jitter (Jitter emittance)
Before
After
J-ARC
e+ target
Linac end:
gbej < 1 μm
J-ARC
e+ target
We focus on dispersion which convert to orbit jitter through energy jitter.
By dispersion correction, jitter emittance become less than 1 mm.
Dispersion
Correction
Y. Seimiya
2. Improvements of emittance growth
Measured
Dispersion
Measured
Jitter emittance
Linac end:
28/7 μm
(Hor./Ver.)
e- beam

## Slide 61: C) Emittance growth caused by Jitter
wake potential induced by target hole (simulation)
Color differences show differences of distance between center of hole and beam position.
Growth factor of beam phase space jitter:
< 0.1@1nC << Measured growth factor
Electron beam straightly pass through the positron generation target hole, whose diameter is 2 mm.
We suspected wakefield effect as a orbit jitter source.
Growth factor〜20
Wakefield effect of target hole is negligibly small.
e-
e+
e-
φ2 mm
14 mm
Target IN
Target OUT
Comparison of orbit jitter
From the beam position before and after target, amplification factor are derived.
LINAC end
2. Improvements of emittance growth
Y. Seimiya

## Slide 62: C) Emittance growth caused by Jitter
Remain orbit jitter can be explained by b function.
Using Twiss parameters measured by WS at sector C, b function near target is derived.
b function is highly correlated with orbit jitter.
We conclude that large orbit jitter sources are mainly both residual dispersion and b function.
Y. Seimiya
2. Improvements of emittance growth
e+ Target

## Slide 63: Other Sources of Jitter
following items were sometimes sources of jitter. Pulsed magnet and RF phase jitter was almost resolved by person in charge.
To identify the jitter source, monitoring beam jitter is important.
x’ [mrad]
x [mm]
Binarization of Pulsed magnet
Slope of RF phase
Near zero cross phase
Near crest phase
Δp/p=0.042%
Δp/p=0.027%
Three valued RF phase
Degree@KL_B3
Degree@KL_C8
Large RF phase jitter cause orbit jitter.
If RF phase is near zero cross, energy jitter is enlarged by the slope of phase.
Y. Seimiya
2. Improvements of emittance growth

## Slide 64: 2. Improvements of emittance growth
Residual dispersion
  Dispersion correction
  Residual dispersion at the acceleration for compression system
Abnormal skew magnetic field from bends
Emittance growth caused by jitters
Other sources
  Wake field in the LINAC
  Radiation excitation in the e- BT line

## Slide 65: Wakefield in Acceleration Structure
Using a steering magnet, we searched an orbit so as to minimize emittance.
Emittance highly depends on beam charge and orbit.
Wake free steering will be performed using RF gun in the next run.
1nC
4nC
Thermionic gun
Y. Seimiya
Notes: 昔のnC変えた時の図を貼る

## Slide 66: Emittance growth induced by radiation excitation in BTe
Simulation | Initial particles | With Radiation | Phase-III final requirement
e- (7 GeV) gbex [mm] | 20 | 65 | 40
e+ (4 GeV) gbex [mm] | 64 | 74 | 100
Particle tracking simulation was performed from the end of LINAC to the end of BT.
Theoretical emittance growth induced by radiation excitation:
∝ g5, 1/r3
Radiation excitation has little dependence on initial emittance.
By the radiation excitation, emittance growth of e-/e+ beam is about 48/10 mm.
The beam size at the injection septum is 0.31 mm, assuming βx = 20 m. The required injection aperture is still dominated by the septum width of 2.5 mm. Although the emittance growth due to synchrotron radiation is very big, it plays only a minor role on the injection aperture itself.
e- beam
M. Kikuchi
gex = 20 mm
gex = 65 mm
Simulation Result
-> The maximum emittance can be relaxed.
Now in re-considering
BT1
BT2
BT2
Y. Seimiya
Notes: Last item is emittance growth induced by radiation excitation in BT for e-.
Theoretical emittance growth induced by radiation excitation is described this equation
and depend on Lorenz gamma to the fifth and inverse of curvature radius to the third.
Particle tracking was performed from the end of LINAC to the end of BT by Ms. Iida.
Initial horizontal emittance of e- and e+ beam have 20 and 64 mm, respectively.
These emittances are increased by radiation excitation and reach 68 and 74 micron.
Especially, electron beam emittance at the end of BT is larger than Phase-III requirement.
Even if the emittance preservation is perfect in the LINAC, emittance growth by radiation excitation
is larger than Phase-III final requirement for the e- beam.
We seek a solution of this problem now.
One possible way is that other tunnel (AR line) is used as electron beam line,
which has smaller ρ than that of current beam line.

## Slide 67: 3. Feedback systems
Orbit feedback
  In front of,
    Jarc, e+ target, Branch to DR, BT, Injection
Energy feedback
  In front of ,
    Jarc, Branch to DR, BT
RF phase
  Master Oscillator feedback between LINAC and MR
  RF phase(partly prepared)
We need more
  Energy spread feedback (using OctoPos-BPM)
  lazer position on the cathode(preparing)
  …
for stability,
are working now.

## Slide 68: Beam abort caused by abnormal injection beam
Abnormal energy beam
Spike and injection beam

## Slide 69
Operation log for SuperKEKB
Additonal information from LINAC
Energy jump
A) Lower or Higher energy injection beam
Beam abort caused by abnormal injection beam

## Slide 70: Fast beam position monitor(BPM) in LINAC
1.Jun.2019 19:56
  LER D6V2 LM abort
Y. Seimiya, F. Miyahara
No energy deviation
Orbit deviation
Dispersive point
Straight line
One station for the power supplies(PS) was set to 0 [A] due to a trigger missing of the PS.
The klystron 51 was down at the time.
The estimation was -46.5 MeV which is consistent with the beam position.
Beam energy was 50 MeV lower.
Injection beam just before abort can be monitored by,
1.Jun.2019 21:19
  LER D6V2 LM abort
Dispersive point
Straight line
Beam abort caused by abnormal injection beam

## Slide 71: Simulations
1.Jun.2019 19:56
1.Jun.2019 21:19
The collimators(CHP, CVP) in the BT could cut the beams with the abnormal orbits.
The lower energy beam(d=-1%) can not be cut in the BT(Energy aperture is ±0.5%) due to the Energy Compression System(ECS) at the end of the LINAC. We have to install one more collimator, which is under planning.
In HER, the collimator for protecting the lower energy beam will be also prepared in this summer.
BT line
BT line
In the both cases, the beams had been injected into the LER.
Y. Seimiya
Beam abort caused by abnormal injection beam

## Slide 72: Lower energy beam through the ECS
DE=０
DE=-50MeV
(d=-1.25%)
LINAC end
Exit of the chicane
Exit of ECS acc. structure
R56=0.9
Since the ECS restores the beam energy, the beam can inject while being shifted in the time direction, which could cause a LER abort.
The longitudinal phase space
d
dz
BT
LER
Beam abort caused by abnormal injection beam

## Slide 73: LER Abort caused by injection beam with higher energy
Phase and HV of KL_51 abnormally changed,
which made 1％ higher beam energy.
It also could inject into LER via ECS.
25.Nov.2019 16:14
4. Beam abort caused by abnormal injection beam

## Slide 74: B) Spike and Injection beam
Still mystery
Injection beams sometimes have some correlation.
  more detailed investigation is needed.
Tunes in LER are also related.
In smaller by*, the spikes increased.
4. Beam abort caused by abnormal injection beam

## Slide 75: Spike and Injection beam
18:03
18:16
18:21
18:24
2019-6-30, by*=2mm
Many spikes were observed.
Injection beam were not the cause in these 4 samples.
4. Beam abort caused by abnormal injection beam

## Slide 76: 2019-11-04 , by*=1mm
Many spikes are observed.
Only one seems to be related to the LINAC orbit.
Beam abort caused by abnormal injection beam

## Slide 77: 2019-11-05 , by*=1mm
4. Beam abort caused by abnormal injection beam
… A few spikes look like to be caused by Injection.
More detail check is needed.

## Slide 78: 5. 2 bunch Injection trial at the last 2 days of autumn run
The BG was high, so we switched back to the single bunch, but it wasn’t only due to 2bunch.
→ After that, BG was improved by LER X-Y coupling correction
The charges of injection were not enough for single bunch especially for HER.
2 bunch injections were tried for both rings.
Total current
HER, LER
Inj. eff. (HER)
Charge for HER
VXD-BW signal
Inj. eff. (LER)
Charge for HER
VXD-FW signal
Belle II
Diamond signal

## Slide 79
1+2 bunch @11.5Hz
1 bunch @11.5Hz
Detail tunings for 2 bunch operation are scheduled in the next February.
BT1ｐ | #1 / 2 bunch op. | #1 / 1 bunch op.
gex [mm] | 198.6±10.7 | 168.0±25.5
gey [mm] | 12.4±2.4 | 12.6±1.5
5. 2 bunch Injection
LER 2 bunch

## Slide 80: Summary
Fire recovery, simultaneous top-up injections, RF-gun deployment, went well
Beam sources and other subsystems are gradually upgraded
Beam controls are being improved based on injection observations
Further beam studies are indispensable balancing the resources and requirements in SuperKEKB complex

## Slide 81
SuperKEKB
dual rings
Mt. Tsukuba
Linac
PF-AR
PF
Thank you

## Slide 83: Summary and plan
Beam operation status
  Achievement of stable simultaneous top up injection to 4 storage rings (HER, LER, PF, and PF-AR) w/ thermionic gun, rf gun, pulsed magnets.
  Energy feedback, orbit feedback loops, dispersion correction, and other operation tools are working fine.
  Pulsed magnets work fine. Pulsed bends will be replaced by new ones to solve heating issues (50 Hz operation) in summer of 2020.
e- beam
  HER injection has been done w/ only rf gun from Phase III day 1.
  Laser system has no significant fault.
  Photocathode: Ir7Ce2 => Ir2Ce (summer of 2019) for higher Qe, however, bunch charge gradually decreased.
  In this winter shutdown: back to Ir7Ce2 photocathode
  Better vacuum for rf gun improvement in summer of 2020.

## Slide 84: Summary and plan (cont’d)
e+ beam
  Flux concentrator has no significant fault.
  New flux concentrator will be installed for higher e+ bunch charge.
Injection background, emittance issues
  Iida san’s talk
  e+ beam emittance growth in BT was much improved in the 2019 autumn run. (ECS magnets at linac end were realigned in summer of 2019)
Low emittance beam w/ high bunch charge
  e- beam emittance growth in Sector2: Steering magnets and BPMs will be installed in e+ capture section (solenoid section).
  Alignment, movable girder of acc. structure and pulsed magnets.
  Precise orbit control, wake field free steering, other beam handling methods.
  Reproducibility of emittance and other beam quality

## Slide 85: 6. Summary and Future plan
Emittance
  e- beam
    The emittance just after the RF gun is OK.
    Investigate emittance growth in the LINAC and BT
  e+ beam
    Almost done for Phase3.3.
    Further studies will be done for the final emittance and charge.
Stability
  e- beam
    To be resoled. -> Satoh-san’s talk
    ( e- damping ring ? )
  e+ beam
    Very stable thanks to the DR.
    Additional collimators will be installed for cut the abnormal energy beams.
  Monitors
    Orbit feedback
      Higher accuracy BPMs synchronized with LINAC shot by shot events in BT will be prepared in a near future.
    Energy spread monitor
      For energy spread feedback, non-destructive beam profile monitors (OctoPos BPM) will be available soon.
      Digitization of energy spread with OTR, etc, will be prepared.
    Bunching
    Diagnostic lines are under consideration.

## Slide 86: Backup slides

## Slide 87
QCS Quench &
e- beam Tuning
VDX BW135
became
“Super clean”.
before tuning
after
tuning
gex=147mm
gey=262mm
gex=99mm
gey=68mm
Energy spread
Energy spread
M. Yoshida
Phase3.1
2019b(Spring)
1. Injection efficiency and background
HER

## Slide 88: (1) Injection beam
 | Tool | Place | Achievement | Feedback | Talk
Energy | (A) Energy feedback | Jarc, DR, BT | ◯ |  | 
Energy spread | (B) Sub Hermonic Buncher 1 (SHB1) for LER beam | Thermionic Gun | ◯ | ー | 
 | SHB2 |  | TBI | ー | 
 | RF Phase monitor | LINAC | ◯ | TBI | T. Miura
 | RF Induced wave monitor | LINAC | △ | ー | 
 | OctoPos BPM monitor | Jarc | ◯ | TBI | F. Miyahara
 |  | BT | △ | TBI | 
 | (C) Temperature control | LINAC | △ |  | 
Orbit | Orbit feedback | LINAC | ◯ |  | Y. Seimiya
 |  | End of BT | ◯ |  | 
Orbit jitter | (D) Pulsed magnet PS | Sector 3-5 | △ | ー | Y. Seimiya
Energy jitter | (D) Energy knob phase | Sector B, 2, 5 | TBI | ー | 
 | (D) RF phase | LINAC | △ | ー | T. Miura
Injection phase | FB of Master oscillator | LINAC and MR | ◯ |  | 
Emittance | (E) e- RF gun | RF Gun | △(Stability) | TBI | R. Zhang
 | e+ DR | DR | ◯ | ー | 
 | (E) Wire scanner | LINAC, BT | ◯ | ー | Y. Seimiya
 |  | End of BT | △ | ー | T. Mori
I. Injection background
TBI: To be introduced
Improvements for stabilizing the injection beam
B
A
C
D
E

## Slide 89: (A) Energy Stabilizer (Energy FB)
BT
Target
Energy knob
Beam energy
( monitored)
±0.03%
Jarc
FB ON
FB ON
Diamond
became small
Beam Energy
±0.1%
±0.05%
CLAWS
Energy FB did not work well.
Diamond Dose
The injection energies have been stabilized within ±0.03%(p-p) by the energy feedback.
I. Injection background
Phase2
T. Kudo,
M. Kikuchi

## Slide 90: (B)Phase fluctuation of SHB1
The long electric cable for 114MHz oscillation replaced to an optical fiber.
The diunal diference due to the phase change almost disappeared.
T. Miura
SHB1 PF
SHB2 PF
green：SHB1 Phase
red: SHB2 Amplitude
SHB2 primary e-
SHB1 primary e-
2.5days
2.5days
2deg.
2deg.
2deg.
2deg.
Tuning
May/13/2019
9:00
After worked, SHB1 becomes stable.
SHB2 is still moving.
I. Injection background
SHB1
SHB2
The fluctuation of SHB depends on the charge from the thermionic gun.

## Slide 91: (D) Beam jitter (cause and remedy)
Binarization from the Pulsed Magnets
  The power supplies will be repaired in this summer.
Binarization from the RF Phase
  Connector or Cable Problems
Large variation of RF phase near the zero cross
  Use the energy knob closer to the top of the RF wave
Before tightening the cable
After
18:00
20:00
1.5°
0.8°
Std=0.28°
Std=0.15°
T. Miura, T. Matsumoto
Progress of LINAC in autumn, 2018
Beam energy stabilization
I. Injection background
Before
After
Orbit stabilization
The cables are exchanged to soft ones.

## Slide 92: C) Beam Jitter caused by hardware equipments
1nC
Linac end:
28/7 μm
(Hor./Ver.)
J-ARC
e+ target
In 2018, large orbit jitter was measured (1000 shots).
Emittance estimated from beam jitter, called jitter emittance, was not negligible.
Orbit jitter (RMS)
Emittance growth converted from beam jitter
m
LINAC end
Design beta function
Bjmag (≧1) express amount of mismatching between beam optics and the jitter optics.
2. Improvements of emittance growth
Notes: \epsilon_{eff} &= \sqrt{ \epsilon_{0}^2 + \epsilon_j^2 + 2\epsilon_{0}\epsilon_jB_{jmag}} \\
& \ge \epsilon_{0} + \epsilon_j

## Slide 93
LER:1bunch
HER:2bunch
LER:1bunch
HER:2bunch
4. 2 bunch Injection
Rep.rate
Injection
efficiency
Charge at BT
Inj. Rate
Total current
LER
HER

## Slide 94
Thank you