## Slide 1: Injector progress and Stable injection
Feb. 4, 2019
32nd B2GM
N. Iida
for SuperKEKB LINAC group

## Slide 2: Contents
Injection background (BG) during Phase 2
Progress of LINAC study for autumn, 2018
  Mainly about the study related to BG
Injection beam for the beginning of Phase 3
Summary
0. Introduction

## Slide 3: LINAC Layout
SuperKEKB-LER
SuperKEKB-HER
DR
LTR
RTL
Sector2
Sector3
Sector4
Sector5
Sector1
SectorA
SectorB
SectorC
Beam Transport lines
(BT)
Jarc
e+
e-
e- Guns
e+ Target＋
Flux Concentrator (FC)
4GeV
7GeV
1.1GeV
Request of injection beam from SuperKEKB |  |  | 
 | Phase 2 | Phase3 Goal | 
 | 2018 | 2019〜202? | 
 |  | e+ | e-
gex [mm] | < 200 | < 100 | < 40
gey [mm] | < 40 | < 15 | < 20
sd [%] | 0.16 | 0.16 | 0.07
Charge [nC] | 1.5 | 4.0 | 4.0
We are here
The goal emittances and charges are gradually improved as by* is squeezed.
0. Introduction

## Slide 4: Injection Beam at KEKB and SuperKEKB
Comparison between the achievement at KEKB and requirement at SuperKEKB Phase 3 goal
  Much smaller emittance even with 3 times higher beam charge.
  Still a big challenge that must be resolved.
Charge (nC)
Norm. Hor.
Emit. (μm)
5
4
3
2
1
0
400
300
200
100
0
0.08
0.06
0.04
0.02
0
σδ(%)
1/7
1.3 times
400
300
200
100
0
Norm. Ver.
Emit. (μm)
1/15
3 times | 
Electron beam for the HER
0. Introduction

## Slide 5: Simultaneous Injection LINAC Beam
Positron
Target
A
B
C
1
2
3
4
5
1.5 GeV e-
1.1 GeV
DR
DC Magnets
Pulsed Magnets
Ring | Energy [GeV] | Charge/bunch [nC] | # of Bunch | Rep. Rate [Hz]
LER | 4 | 4 | 2 | 50
HER | 7 | 4 | 2 | 50
PF-AR | 6.5 | 0.3 | 1 | 25
PF | 2.5 | 0.3 | 1 | 25
Beam injection with pulse-to-pulse variable charge and energy
Device parameters change at 50 Hz (20 ms)
Pulsed magnets commissioned at 3-5 sectors (2017 autumn), and many more have been installed also in this winter.
deceleration
positron target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
the same energy
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 4 GeV e+
variable energy pulse-to-pulse
Sector#
0. Introduction
Achievement:

## Slide 6: Merger Line (Sector A)
Thermal gun
  LER, PF, PF-AR (, HER)
  Thermal gun
  SHB1(114MHz)
  SHB2(571MHz)
  Pre-buncher
  Buncher
  Accelerating Structure(2mx2)
24 degree Merger Line
  The beam of the thermionic gun joins at the merger line.
RF gun
  HER
  0-deg QTW RF gun
  90-deg CDS RF gun
  Bunch Compress System(BCS)
  Accelerating Structure(2mx1)
T. Kamitani
24 degree Merger line
Thermal Gun
RF Gun
LER
PF
PF-AR
HER
Bunching Section
0. Introduction

## Slide 7: Contents
Injection background(BG) during Phase 2
Progress of LINAC study for autumn, 2018
  Mainly about the study related to BG
Injection beam for the beginning of Phase 3
Summary
0. Introduction

## Slide 8: １．Injection BG in Phase 2
Tuning of collimator in the MR has been very useful for suppressing the BG.
A stable beam is very important to reduce the BG;
  Beam energy (Energy FB)
  Energy spread
  Energy jitter
  Orbit in LINAC, BT
  Optics, Emittance
Tools to be prepared;
  LINAC orbit FB (Phase 3)
    Now preparing
  RF phase/voltage monitor
  Energy spread monitor
Background TF Report (2018105) for B2GM
1. Injection BG in Phase 2
Beam Energy
Energy Spread
Energy Jitter
These will be talked
the next topic

## Slide 9: A) Energy Stabilizer (Energy FB)
BT
The injection energies have been stabilized within ±0.03% by the energy feedback.
Target
Energy knob
Beam energy
( monitored)
±0.03%
1. Injection BG in Phase 2
Jarc
FB ON
FB ON

## Slide 10: B) Energy spread
Arc section in Beam Transport line (BT)
Before tuning
After tuning
The energy spread can be monitored only by destructive screen monitors. → A nondestructive monitors are necessary.
RF Phase drifts due to temperature change.
Temperature
in HV station of the thermal gun
Temperature
of atmosphere
Room temperature
of the thermal gun
Energy spread is very sensitive to the RF phase.
→ RF phase/voltage monitors are necessary.
1. Injection BG in Phase 2
Energy spread was widened.
7/13 20:00
7/13 20:43
Energy spread

## Slide 11: C) Energy jitter
Diamond became small
After suppressing the energy jitter,
the signal from Diamond detector was reduced.
Energy Jitter
±0.1%
±0.05%
CLAWS
B2GM_Background TF_2018105_Iida
Beam background is sensitive to the energy jitter.
1. Injection BG in Phase 2
Energy FB did not work well.

## Slide 12: Contents
Injection background(BG) during Phase 2
Progress of LINAC study for autumn, 2018
  Mainly about the study related to BG
Injection beam for the beginning of Phase 3
Summary
0. Introduction

## Slide 13: LINAC Beam Studies (Oct.-Dec., 2018)
RF Gun (M. Yoshida, X. Zhou, R. Zhang )
Thermionic Gun
  Tuning of Buncher (T. Natsui)
  Q-Scan、10nC（T. Natsui and Y. Seimiya）
24 degree Line
  Measurement and Correction of Dispersion（Y. Seimiya）
  Measurement of Response and Aperture (Y. Seimiya)
  Consistency Measurement of BPM (F. Miyahara)
Jarc
  Measurement and Correction of Dispersion（Y. Seimiya）
  Bunch Compress（M. Yoshida)
  OctoPos BPM (F. Miyahara)
Measurement of Beam Position Jitter and Fluctuation (Y. Seimiya)
  Binarization from Pulsed Magnet (T. Natsuim Y. Enomoto, M. Satoh, I. Satake)
  Monitors of RF Phase and RF Induced wave
Monitors of RF Phase and RF Induced wave (T. Miura, et al.)
Primary side power fluctuation (T. Miura, T. Natsui)
Investigation around Dummy Target (Y. Enomoto, H. Sugimura, T. Kamitani, Y. Ohnishi, Y. Funakoshi, N. Iida)
  Beam Based Aligment ( Ballistic Orbit、QuadBPM )
Investigation of Solenoid magnet after Positron Target (T. Kamitani, Y. Ohnishi)
Measurement of RF Energy Gain (T. Kamitani, Y. Ohnishi, T. Natsui, Y. Seimiya, M. Satoh)
SY2 (N. Iida, H. Koiso)
  Measurement of Dispersion
Sector 3-5
  Offset Injection (Y. Seimiya, N. Iida, T. Mimashi, T. Kawamoto, K. Yokoyama)
  Fudge Factor Measurement of Quad (Y. Seimiya, M. Satoh )
  QuadBPM (H. Sugimura), Mover Alignment (Y. Enomoto, T. Kamitani)
Coexistence with PF and PF-AR
… Studies especially related to the BG:
Core subjects

## Slide 14: 2. Progress of LINAC in autumn, 2018 related to the BG
Jitter of beam position
Beam energy stabilization
  RF phase/voltage monitor
  RF Stabilization
Energy spread monitor
  “OctoPos”: Eight electrode BPM
Tuning of the bunching
Energy spread, jitter: broad
DE/E
Z
sd
Energy spread, jitter: narrow
DE/E
Z
sd
2. Progress of LINAC in autumn, 2018
RF voltage
RF voltage

## Slide 15: (A) Jitter of beam position
Y. Seimiya
J-ARC
hx ~ 0.8 (m)
Horizontal
Vertical
e+ target
There is a problem of the beam position jitter after the positron target.
A hole in the positron target for HER e- beam： f2 mm．
  Possibly the small hole could have caused the position jitter ?
Phase space plot at BPM after target.
Phase space plot at BPM before target.
2. Progress of LINAC in autumn, 2018
Horizontal
Vertical
Sector
5
Sector
C

## Slide 16: Jitter of Beam Position
A hole in the positron target for HER e- beam： f2 mm．
  Possibly the small holes could have caused the position jitter ?
LINAC Study in Autumn, 2018
  A movable dummy target was installed instead of the positron target.
  Beam studies were done with in/out the dummy target.
The positron target was re-installed now.
Y. Enomoto
plan view
2. Progress of LINAC in autumn, 2018
for HER
for LER

## Slide 17: Removed the Flux Concentrator (FC)
SP_15_T
SC_15_T
GV_15_T
BY_13_5
PY_13_5
Y. Enomoto
(LCG meeting, ‘18/7/2)
2. Progress of LINAC in autumn, 2018

## Slide 18: Installed a dummy target block
SP_15_T
SC_15_T
GV_15_T
BY_13_5
PY_13_5
Y. Enomoto
(LCG meeting, ‘18/7/2)
2. Progress of LINAC in autumn, 2018

## Slide 19: Jitter Emittance
With Target hole(φ2mm)
No Target hole
The growth of the jitter emittance has been nothing to do with the small hole.
Strong correlation between orbit jitter and beta function.
The beta function after the target is large to squeeze the beam sizes to pass through the hole, which causes the large orbit jitter.
The result is;
2. Progress of LINAC in autumn, 2018
Although the jitter emittances are still increased as shown in the jitter emittance plots, it is known that this jitter becomes smaller when Jarc's dispersion leakage is reduced.
They are small enough at the end of LINAC.
Position jitters x, y [mm]
√bx, √by

## Slide 20: Beam Jitter Sources
Binarization from the RF Phase
(at the dispersive section)
Degree@KL_B3
Degree@KL_C8
Y. Seimiya
Causes of several beam fluctuations were revealed by BPMs and the new RF monitors.
②
Large variation of Energy gain
near zero cross of RF phase
near zero cross
near peak
Δp/p=0.042%
Δp/p=0.027%
③
x’ [mrad]
x [mm]
Binarization from the Pulsed Magnets
(at the straight section)
①
2. Progress of LINAC in autumn, 2018
RF phase monitor
Beam energy (arb. unit)

## Slide 21: Beam jitter (cause and remedy)
Binarization from the Pulsed Magnets
  Currently under investigation
Binarization from the RF Phase
  Connector or Cable Problems
Large variation of RF phase near the zero cross
  Use the energy knob closer to the top of the RF wave
Before tightening the cable
After
18:00
20:00
1.5°
0.8°
Std=0.28°
Std=0.15°
T. Miura, T. Matsumoto
2. Progress of LINAC in autumn, 2018
(B) Beam energy stabilization

## Slide 22: Cable re-connection
Before
After
In the cable connection before work, since the cable was hard and thick, a force was applied to the connecting part, causing poor contact between the cables.
By holding a soft cable in between, the cables felt less stress any more.
In this winter shut down, some other connectors were re-connected.

## Slide 23: Other voltage fluctuation of klystron power supply
C1: RF voltage
C1: RF Phase
7deg
5%
RF voltage / phase variation
Klystron output power is stabilized by
Induced Voltage Regulator (IVR) at the sudden change of AC line voltage.
In Phase 2, IVR stabilization had been done once an hour.
It is planed to establish the IVR feedback in Phase 3.
2. Progress of LINAC in autumn, 2018
Sometimes the AC line voltage for klystron power supply drops.
(B) Beam energy stabilization

## Slide 24: （C) Nondestructive Energy Spread Monitor： “OctoPos”, eight electrode BPM in Jarc
The beam spread can be measured from the second moment.
Second moment and horizontal profile
F. Miyahara
sx monitored with
screen monitor
sx monitored with
OctoPos BPM
Although the profile with two peaks ② can not be recognized from ⑥ only with the second moment, it is important to keep the energy spread to ③ or ④.
We would like to use this monitor in Phase 3.
2. Progress of LINAC in autumn, 2018
①
②
③
④
⑤
⑦
⑥
There are two more OctoPos in the BT.

## Slide 25: (D) Bunching after the thermal gun (Simulation)
optimized value: s=7.6 psec
T. Natsui
The beam dynamics in the bunching section is simulated with the GPT code.
2. Progress of LINAC in autumn, 2018
Bunch length

## Slide 26: (D) Bunching after the thermal gun (Beam study)
Oct. 29 Tuning with 10 nC-beam
20 psec
No satellite bunch around the beam
SHB1 : 9.4 kW, SHB2 : 3.2 kW
Nov. 22
Some satellite bunches were observed.
The satellite bunches appeared, while the phases of the bunchers were not changed．
By the RF phase drift？
T. Natsui
After 3weeks
We would like to monitor the phase drift of the SHB which can affect the BG due to the satellite.
2. Progress of LINAC in autumn, 2018
The bunch length is short enough.
Monitored bunch length with a streak camera

## Slide 27: Contents
Injection background(BG) during Phase 2
Progress of LINAC study for autumn, 2018
  Mainly about the study related to BG
Injection beam for the beginning of Phase 3
Summary
0. Introduction
3. Injection beam for the beginning of Phase 3

## Slide 28: 3. Injection Beam for the beginning of Phase 3
Charge and Repetition Rate (Max.)
  LINAC RF: 50Hz
  HER : 2nC, 25Hz, 2 bunches
  LER : 2nC, 23Hz=25Hz-2Hz(PF+AR), 2 bunches
  They are enough for the top-up injection.
Emittance Preservation
  The big issue for the BG.
3. Injection beam for the beginning of Phase 3

## Slide 29: Merger Line (Sector A)
Thermal gun
  LER, PF, PF-AR (, HER)
  Thermal gun
  SHB1(114MHz)
  SHB2(571MHz)
  Pre-buncher
  Buncher
  Accelerating Structure(2mx2)
24 degree Merger Line
  The pulsed bends for 25 Hz are available now.
  50 Hz operation will be ready in 2020 summer.
RF gun
  HER
  0-deg QTW RF gun
  90-deg CDS RF gun
  Bunch Compress System(BCS)
  Accelerating Structure(2mx1)
T. Kamitani
24 degree merger line
Thermal Gun
RF Gun
LER
PF
PF-AR
HER
3. Injection beam for the beginning of Phase 3
Pulsed bends

## Slide 30: Lifetime and injection rate
Example : Phase 3-3ex Parameter
 | LER | 
Life time [sec.] | 600 | Nb=1578, Itot=2.0A
Loss Rate [mA/sec] | 3.0 | 
frev=100kHz
QBTend=1.0nC
frep=25Hz
nbunch=2
effinj=70%
Even if such a low charge injection, the total beam current can be kept
with 25Hz injection.
3. Injection beam for the beginning of Phase 3
Assumed from the lifetime of Phase 2

## Slide 31: Emittance blowup in Phase 2
B C
5 BT
B C
5 BT
B C
5 BT
B C
5 BT
DR designed value
Final Request from MR
Phase2 ----------
Phase3 ----------
e-
e+
X
Y
40 ----
15 ----
Measurement at the upstream of BT
0.7nC
1.2nC
More beam studies at BT will be needed.
There is no question that the emittance blowup affects the BG.
3. Injection beam for the beginning of Phase 3

## Slide 32: Linac Schedule Overview as of Jun.2018
RF-Gun e- beam
commissioning
at A,B-sector
e- commiss.
at A,B,R,C,1
e+ commiss.
at 1,2 sector (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 sector
non damped e+ commiss.
at 1,2, 3,4,5 sectors
e- commiss. at A→5 sectors
damped e+ commiss.
at 1→5 Qe+ = 1~4nC
e- commiss.
at A→5 Qe- = 1~4nC
: Electron
: Positron
: Low current electron
1 - 2 nC
Phase2
1 nC
Phase1
Location
↓
Time →
Phase1: high emittance beam for vacuum scrub
Phase2,3: low emittance beam for collision
Schedule
Without Top-up
1 - 4 nC
Phase3
Improved RF gun
Direct PF-AR BT
DR Commiss.
Beam Licenses in steps
Low Emittance Beams
4+1 Ring
Injections
Low Emittance Injections
There is no future schedule for a big modification now.
Summer
2020
24 degree line
ready for
50Hz operation

## Slide 33: 4. Summary
Injection background(BG) during Phase 2
  The deviations of the injection beam mainly related beam energy could be the BG source.
Progress of LINAC study for autumn, 2018
  The voltage and phase monitors of RF, OctoPos BPM are powerful tools.
  In Phase 3, we would like to use them to test and operate feedback tools.
Injection beam for the beginning of Phase 3
  The charge and repetition rate are enough for Phase 3-3ex.
  The studies for the emittance preservation are needed in LINAC and the BT.
  More studies for LINAC including BT are indispensable !

## Slide 34: Backup

## Slide 35: Life and minimum injection
Example 1:
 | LER | 
Life time [sec.] | 1200 | Nb=1578, Itot=1A
Loss Rate [mA/sec] | 0.83 | 
frev=100k
QBTend=1.0nC
frep=25Hz
nbunch=1
effinj=70%
Even if such a low charge injection, the total beam current can be kept
with 25Hz injection.

## Slide 36: Lifetime and injection rate
Example :
 | LER | 
Life time [sec.] | 670 | Nb=1578, Itot=1.8A
Loss Rate [mA/sec] | 2.6 | 
frev=100k
QBTend=1.0nC
frep=25Hz
nbunch=2
effinj=70%
Even if such a low charge injection, the total beam current can be kept
with 25Hz injection.
Phase 3-3 Parameter
3. Injection beam for the beginning of Phase 3