## Slide 1: Electron / Positron Injector Linac Status
Kazuro Furukawa
<kazuro.furukawa@kek.jp>
for Linac division

## Slide 2: Mission of electron/positron Injector in SuperKEKB
40-times higher Luminosity
  Twice larger storage beam  Higher beam current at Linac
  20-times higher collision rate with nano-beam scheme
     Low-emittance even at first turn  Low-emittance beam from Linac
     Shorter storage lifetime ( Higher Linac beam current)
Linac challenges
  Low emittance e-
    with high-charge RF-gun
  Low emittance e+
    with damping ring
  Higher e+ beam current
    with new capture section
  Emittance preservation
    with precise beam control
  4+1 ring simultaneous injection
2x beam current
40x Luminosity
RF-gun
e+ efficiency
Linac Overview
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: Facility Upgrade
Addition of electric power and cooling water is crucial for the upgrade
  However, the facility division starts the design only after the budget is secured
  It was only approved in JFY2012 (the facility budget is different from the project one)
Basic schedule
  Design JFY2012, Building JFY2013, Facility JFY2014
  Should not affect PF and PF-AR operation
  Not available during initial commissioning
4.0 GeV e+ 4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
high current
gun
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
RF gun
e+ target &
capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER
C-band
modules
3T
RF gun
Linac Facility
    Positron capture section
    920 kVA, 900 lit/min
PF-AR
6.5 GeV e-
    Damping ring BT (LTR, RTL)
    310 kVA
    Switch yard (3SY)
    300 kVA, 460 lit/min
Ohsawa et al.

## Slide 4: Girder Recovery and Alignment
Re-constructing soft-structure girder into hard-structure
Alignment with
  120m and 480m long-baseline laser between girders
  Laser tracker within a girder (~20m)
  Beam-based tests
  Target: 0.1mm local / 0.3mm global alignment (from beam dynamics simulation)
    Several iterations necessary for low-emittance beam transport
Beam transport/acceleration test for 600m (Nov.2012)
  For the first time after the earthquake
X
Y
Charge
Beam along 600-m linac
Higo et al.
Girder Distortion
Girder Reinforcement

## Slide 5: Microwave Power Source Upgrade
Pulsed power modulators
  Nine compact modulators are introduced
  Share the same basic design for klystron, flux concentrator, and gun high voltage
Fast LLRF controllers, power amplifiers, and LLRF monitors
  For simultaneous injection and bucket selection
  Pulse-to-pulse stability monitor
  50Hz event-based synchronized controls
Michizono et al.

## Slide 6: RF Gun Development
Photo cathode : stability, longer life, efficiency
  At first LaB6, then Ir5Ce  5nC / bunch
Laser : higher power, temporal profile control
  Nd:YAG medium, LD excitation  ~1.5mJ / 30ps / pulse at 266nm
  Polarization control for slant irradiation
  Yb:YAG fiber laser is introduced
Cavity : better focusing field, higher gradient
  DAW (Disk and washer) type cavity
  Development of quasi-travelling-wave side-coupled cavity as well
Test stands
  RFgun at A-1 is constructed with fiber laser for SuperKEKB
  RFgun at 3-2 was used to inject into PF with proper synchronization
  Long-period demonstration will be performed
Ir5Ce
DAW
RF Gun for Low-emittance Electron Beam
Yoshida et al.

## Slide 7: Beam Acceleration Test (RF-gun)
Step-by-step beam tests
  4.5nC 240m acceleration
  Fiber-laser-based RF-gun
X
Y
Charge

## Slide 8: Positron Capture Section Development
Flux concentrator (FC)
  Collaborations with BINP, IHEP and SLAC
  Finalized optimization of field and mechanical design
  Fabricated 1st version of 2nd generation, being tested
Large-aperture S-band (LAS) cavity structure
  Positron capture tracking simulation
  L-band structure as backup with co-linear load
Magnet design and fabrication
  Solenoid and pulsed steering and quad magnet system
Reliability
  Strategy for failed component replacement with detachable girder, etc
  Acceleration gradient distribution and optimization with backups
Positron Capture for High-current Positron
LAS
Kamitani et al.
FC

## Slide 9: Beam Monitors: BPM and WS
    Limited performance with present 8-bit 10GS/s digitizers (oscilloscopes)
New BPM readout for precise orbit/emittance controls
  Fast attenuator for 0.1-10nC (SuperKEKB, PF, PFAR) dynamic range
  Helical BSF (300MHz) for 2-bunch (96ns apart) readout
  16bit 250MS/s ADC, FPGA data processing
  50Hz event-control synchronization
New wire scanner readout was also developed
Suwada et al.

## Slide 10: Single Machine, Multiple Virtual Accelerators (VAs)
Simultaneous injection, one of the VAs is active at a time
Independent parameter set for each VA, ~200 parameters are switched every 20ms pulse
ARC
e– (2.5GeV)
e− Gun
ARC
e+ Target
e+ (4GeV)
e− Gun
Event-based Control System
PF Injection
KEKB-LER Injection
Primary e– (3.5GeV)
ARC
e– (7GeV)
e− Gun
KEKB-HER Injection
Dual-layer Controls
ARC
e– (6.5GeV)
e− Gun
PF-AR Injection

## Slide 11: Example of Beam Mode Pattern : e+ 25Hz / e– 25Hz
Interleaved e+ and e-, dependency between pulses mostly decoupled
With bucket selection at the both DR and MR
Dual-layer Controls
ARC
e+ Target
e+ (4GeV)
e− Gun
Primary e– (3.5GeV)
ARC
e+ Target
e+ (4GeV)
e− Gun
Primary e– (3.5GeV)
20ms
20ms
20ms
ARC
e– (7GeV)
e− Gun
ARC
e– (7GeV)
e− Gun

## Slide 12
Preliminary Beam Tests in Autumn 2012
  Beam test along 600-m Linac
  for the first time after the earthquake
  Latter half was tuned for PF/PFAR injection
  Alignment will be recovered by 2014
  For energy spread optimization
  Longitudinal beam profile management
  by photo-cathode RF-gun (30ps square shape)
  and bunch compression at the middle of linac
  are crucial
    Preliminary R56 control
    was performed
    Design and measurement
    of dispersion function
    with R56=0 and R56=-0.6
Measurement
Design
X
Y
Charge
Beam along 600-m linac
R56=0
R56=-0.6

## Slide 13: Schedule
Winter 2013 : DR switchyard / DR tunnel construction
Spring 2013 : A1-RF-gun, Alignment
Summer 2013 : Installation of many components
  ECS, FC (gen.2), DC solenoids, Klystron modulators, WS, etc
Autumn 2013 : e– then e+ commissioning (limited current)
  Half Linac: PF injection, Day: construction, Night: commissioning
Spring 2014 : Pulsed steering, Alignment
Summer 2014 : Installation of additional components
  Cooling water, FC (gen.3), BPM, Pulsed magnets, New PFAR BT, etc
Autumn 2014 : Linac Full Commissioning
Winter 2015 : MR (then DR) injection commissioning
…
Schedule

## Slide 14: Summary
Much progress in disaster recovery and construction
Development for T=0 (~1nC) was mostly completed
Development for full spec. will be tested
Many development items are connected with beam emittance and energy spread management
Still expecting many challenging items to overcome
Injector should start at first !
With some Phronesis (Greek: practical wisdom, ability to understand the universal truth), we believe we can achieve the target

## Slide 15: Thank you

## Slide 16: Review 2013 and Reviewer’s Comments (preliminary)
Overview of Injector Construction Status and Schedule
  The Linac Group setup prioritized work scopes with back-up options. The overall scheme is very logical, and the committee is convinced by their near term plan.
RF gun
  Install and test the QTWSC gun as planned. Operate it for a long period to check its reliability and performance stability.
Alignment and Support
  The Linac alignment and support is less mature. There should be some effort to accelerate this to avoid the possibility of impacting commissioning.
Positron Source
  The target size should fit into the available space between the yoke and flux concentrator. The discharge waveform of the modulator for the flux concentrator with cables should be checked experimentally.
Commissioning (of Electron Beam)
  After identifying the parameters that the linac electron beam needs to meet, a detailed set of procedures should be made for each parameter. An overall time schedule to carry out these procedures should be developed to match times needed by the four rings.

## Slide 17: Review Items in 2012 and Reviewer’s Comments
Linac disaster recovery
  Earthquake is a natural disaster, a Force Majeure. In view of the manpower shortage in the Linac and Storage Ring groups, the committee suggests that the management team look into timeline, milestones and resources, and revise the schedule accordingly.
RF gun and low-emittance transport
  Aggressively pursue a demonstration of the QTW gun with LaB6 cathode and the full power laser.
Positron source
  CSR effects in the bunch compressor should be examined. A protection scheme for the target should be developed at least conceptually.

## Slide 18: Linac Upgrade for SuperKEKB
Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring, Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc
4.0 GeV e+ 4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
high current
gun
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
RF gun
SuperKEKB injector Linac
e+ target &
capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER
PF-AR
6.5 GeV e-
C-band
modules
3T
RF gun
Linac Overview

## Slide 19
Bunch Compression
A
B
C
1
2
3
4
5
HER
7.0 GeV
5nC x 2
20 um
LER
4.0 GeV e+
4nC x 2
Primary e– for e+
3.2 GeV, 10nC x 2
1.1 GeV
e+ damping ring
Energy Compression
Bunch Compression
PF
2.5 GeV
0.1nC x 1
New RF-gun
5 nC for e–, 10nC for e+ IrCe cathode, Fiber laser, DAW cavity
New e+
Capture
with FC
PF-AR
6.5 GeV
5nC
J-arc
1.5 GeV
Energy Compression
SY2
SY3
Linac Upgrade for SuperKEKB
electron
beam
positron
beam
Flux
Concentrator
As a high-field (several Tesla) pulsed solenoid for the positron source of the SuperKEKB injector, KEK is going to fabricate a SLAC-type flux concentrator.
Technical advices from the IHEP experts and design information by the IHEP drawings are quite useful in the development.