## Slide 1: Middle Layer Services at NSLS II for Beam Commissioning and Operation
Guobao Shen
Controls Group, Photon Sciences
Brookhaven National Laboratory
Feb, 2014

## Slide 2: Content
NSLS II Overview
NSLS II Control Brief
Virtual Accelerator
EPICS V4 based Middle Layer Service
RESTful based Middle Layer Services
Beam Commissioning
NSLS II Construction
Conclusion

## Slide 3: NSLS II Overview
Injection Straight Section
200-MeV linac
15 nC/160-300 ns,
0.5% e.s., 50 µmrad
LBT: 150nm-rad (4σxσx’)
0.5% energy spread
Single bunch 0.5nC/sec
Multibunch (15nC/sec, 80~150)
3-GeV booster, C=158m
20 mA, 1 Hz, 40 nmrad
BST: 50nm-rad
0.1% energy spread
8nC/sec
Injection system
  Turn key: LINAC & Booster

## Slide 4: NSLS II Overview
Beam Specifications | 
Energy | 3.0 GeV
Circumference | 792 m
Number of Periods | 30 DBA
Straights | 6.6/9.3 m
Emittance (h,v) | < 1/0.008 nm
Momentum Compaction | 0.00037
Dipole Bend Radius | 25 m
Energy Loss per Turn | <2 MeV
Energy Spread | 0.09%
RF Frequency | 500 MHz
Harmonic Number | 1320
RF Bucket Height | >2.5%
RMS Bunch Length | 15-30 ps
Average Current | 500 mA
Current per Bunch | 0.5 mA
Charge per Bunch | 1.2 nC
Touschek Lifetime | > 3hrs
Storage ring parameters
  30 Cell DBA lattice structure
Courtesy of Weiming Guo

## Slide 5: NSLS II Controls Brief
System Architecture
Distributed Front-Ends
CAS PVAS
Diag db
CAS PVAS
PS db
CAS PVAS
RF db
Physical Device
Physical Device
Physical Device
CAS PVAS
VA db
Physical Device
CAS
JMS Service
Tracy-III Simulation
MySQL/IRMIS
PVAS
HTTP/REST
Lattice/Model
Python
MySQL
PVAS
HTTP/REST
Channel Finder
Java
MySQL/IRMIS
PVAS
HTTP/REST
MUNICONV
Python
SQLite/IRMIS
EPICS V4
MASAR
Python
Ethernet
Python Apps
CAC PVAC REST
MMLT
CAC PVAC REST
Matlab Apps
CAC PVAC REST
Channel Arch
CAC PVAC REST
CS-Studio
pvManager
CAC PVAC REST

## Slide 6: NSLS II Controls Brief
Control room software
  Debian/Linux 7 consoles
    4 for general operator and 1 for lead operator
  Python cothread for channel access
    Version 2.8/Python 2.7
  Dedicated matlab server
    3 for physicist
    1 for BPM expert
    labCa 3.4 support
  Elegant/SDDS install
    Limited support

## Slide 7: Virtual Accelerator
Distributed Front-Ends
CAS
JMS Service
Tracy-III Simulation
Ethernet

## Slide 8: Virtual Accelerator
An integrated accelerator simulation code
  Provide real time accelerator simulation results
A standalone EPICS V3 IOC
Virtual accelerator at NSLS II
  Uses Tracy-3 as simulation backend
  Provide realistic accelerator beam behavior
    Integrate realistic lattice
    Integrate misalignment
    Emulated setting jitter for magnets

## Slide 9: Virtual Accelerator
Main purpose
  Support high level application development
    Especially physics application development
    All simulation results available via EPICS V3 PVs
  Middle layer service development
    Channel finder service
    MASAR service
    …
  Other tool need EPICS V3 PVs

## Slide 10: Virtual Accelerator
What does it do?
  All data via EPICS PVs
    Beam Optics
    Hardware setting & read back
  Adjust setting of each device individually
    Magnets: Bend, Quad, Sext, Correctors, …
    RF frequency & voltage
    Insertion device for synchrotron machine
  Dynamically change hardware setting
  Real time simulation
    Simulation performed continuously

## Slide 11: Virtual Accelerator
What does it do?
  Errors source
    Engineering ripple
      magnet setting
      BPM read back
    Misalignment
  Read back beam behavior
    Beam position at each BPM
    Beam closed orbit
    Beam optics TWISS parameters

## Slide 12: Virtual Accelerator
What does it not do or need many effort to do?
  Other accelerator behavior not available via a simulation code
    Vacuum reading
    Mechanical moving
    Ground vibration
  Multiple particle tracking
    Performance issue
  Synchrotron photon laser behavior

## Slide 13: Virtual Accelerator
Automatic generate EPICS database
  Load a lattice file in
  Apply NSLS II naming conversion
  Generate EPICS .db file
  Generate cmd file to initialize each setting point PV
  Generate a table to descript the property
    for physics application
    For channel finder services
Notes: Table could be used to pop up properties in channel finder for each PV to enable minimum efforts to switch apps from va to real machine
More details could be in a ICALEPCS13 paper

## Slide 14: EPICS V4 based Middle Layer Service
CAS PVAS
Diag db
CAS PVAS
PS db
CAS PVAS
RF db
Physical Device
Physical Device
Physical Device
CAS PVAS
VA db
Physical Device
CAS
JMS Service
Tracy-III Simulation
SQLite/IRMIS
EPICS V4
MASAR
Python
Ethernet
Distributed Front-Ends

## Slide 15: EPICS V4 based Middle Layer Service
An international collaboration working group
  Collaborative institutes
    APS
    BNL
    COSYLAB
    DLS
    PSI
    SLAC
    ESS
  Weekly telecon meeting
  A nominal 4 months face-face meeting rotating between the developer’s sites.

## Slide 16: EPICS V4 based Middle Layer Service
An open source project for experimental facility
  Extension of EPICS version 3
    Complex data structure/data types
    New communication protocol
  Expanded to fitting the requirement
    Physics middle layer server
    Data acquisition
    Experimental control
    Other general service

## Slide 17: EPICS V4 based Middle Layer Service
V4 Modules
  Core modules:
    pvData: fundamental data structure
    pvAccess: communication protocol, carry data on wire
    pvCommon: common utility library
  Extensions
    pvaSrv: EPICS Base IOC plugin interfacing V3 data to pvAccess
    Normative type: collection of pvData data types that may be used for general purpose
  Service modules:
    Developed at each different site for its own purpose
  Language support
    C++ & Java mainly
    Python, but greatly behind because of short of man-power

## Slide 18: EPICS V4 based Middle Layer Service
EPICS Database
Device Support
Device Driver
Channel Access
Channel Access
Channel Access Client
Client Apps
pvaSrv
pvAccess
Channel Access
Client Apps
pvData
V4 processing engine
Normative Type
Channel Access
pvAccess Client
Client Apps
pvAccess
Interoperation with V3

## Slide 19: EPICS V4 based Middle Layer Service
Communication Mechanisms
  Get, Put, Monitor, Command/Response, Broadcast, Multicast
Normative types:
  NT(DBRTypes), NTImage, NTTable, NTMultichannelArray, NTNDArray, NTStatistics,
pvAccess
  optimized to send large arrays and structured data.
pvaSrv
  reference implementations of middle layer services for relational databases or continuous data sources
  serves V3 channels from the EPICS process database as does Channel Access.

## Slide 20: EPICS V4 based Middle Layer Service
pvAccess and Channel Access comparative performance (Number of channel value get operations per second), where only one channel's value is got in each get operation, as a function of array size of the channel
Courtesy of Matej Sekoranja
Notes: The setup is C++ clients and servers, of the Beta 1.0.1 release (as on the downloads page), 2 MacBook Pros (~2GHz Intel Core Duo-s, 4GB memory) with a 1 GBit Ethernet point-to-point connection.

## Slide 21: EPICS V4 based Middle Layer Service
pvAccess and Channel Access comparative performance (Number of channel value get operations per second), where 1000 channels values' are got in each get operation, as a function of array size of the channel.
Courtesy of Matej Sekoranja
Notes: Some earlier performance benchmarking results could be found in BNL tech-report 82, and PAC11 conference paper, MOP252

## Slide 22: EPICS V4 based Middle Layer Service
MASAR
  Machine Snapshot, Archiving, and Retrieve
  A general purpose tool to snapshot data from V3 PVs
  Implemented in V4
  Machine
    A facility controlled by EPICS, accelerator for example
  Snapshot
    Data at specific time point
      Value, time stamp, connection status, alarm status, alarm severity
Similar tools, but different purpose
  IOC automatic save & restore
    IOC bumpless rebooting
  Channel Archiving
    Archive pre-defined configuration periodically
    All data saved time serially

## Slide 23: EPICS V4 based Middle Layer Service
Service Engine
pvAccess/channelRPC
PyQt
Channel Access
Gather/C++
Low Level Python Client Library pvAccess/channelRPC Client (C++)
pvAccess
DSL-PY Module
PYMASAR
(SQLite)
Scripting
IOC
IOC
IOC
Scripting
High Level Scripting API
CS-Studio/BOY
pvAccess Client Library (Java)
Finished
User Apps
Planning
Developing
Others
(Matlab)
MASAR Architecture

## Slide 24: EPICS V4 based Middle Layer Service
Snapshot configuration
  EPICS V3 PV orientated
    Support all scalar and waveform PV types
      Float, double, string, and enum
  PV group
    Collection of PV names
      Can be a mix of any of the types
    One PV can be in many PV groups
  Configuration
    Collection of PV groups, therefore, collection of PV names
    One PV group can be in many configurations
Snapshot
  An event happened at a particular time
  Belongs to one configuration
    One configuration can have many events
  Each event is one data set
    Header information + meta data (value, time stamp)
Notes: With a pre-defined configuration, a client can request MASAR to take a machine snapshot. Once the service engine gets a request, it retrieves the PV list for given configuration from SQLite, requests Gather library (a local Channel Access library implemented in C++ to gather PV data) to get data for each PV, and saves data into RDB via PYMASAR. In addition to the value, the connection status, time stamp, alarm severity, and alarm status for each PV is also saved.

## Slide 25: EPICS V4 based Middle Layer Service
Snapshot configuration
configuration
...
event
event data
pv
pv group
Snapshot

## Slide 26: EPICS V4 based Middle Layer Service
UI PyQt4 based graphic user interface
  Browse configuration
  Browse event
  Take snapshot
  Retrieve data
  Compare data
  Restore machine
  Export data to external file

## Slide 27: EPICS V4 based Middle Layer Service
Event data browsing and comparing with live machine
Notes: Plot waveform data of a cell
Plot multiple data cells of a PV
Plot multiple data cells of selected PVs
Plot all cells of a PV
Plot all cells of selected PVs

## Slide 28: EPICS V4 based Middle Layer Service
Multiple data sets comparison
    Support up to 9 data sets
Notes: User select data set to be compared
Select reference data set from a pop up dialog
By default, first selected data as reference set

## Slide 29: EPICS V4 based Middle Layer Service
Waveform data
Notes: Plot waveform data of a cell
Plot multiple data cells of a PV
Plot multiple data cells of selected PVs
Plot all cells of a PV
Plot all cells of selected PVs

## Slide 30: EPICS V4 based Middle Layer Service
Deployed in control network from the first day (3/27/2012)
Configuration increasing over time (by Jan 15 2014 10:51 AM)

## Slide 31: EPICS V4 based Middle Layer Service
Snapshots taken over time (by Jan 15 2014 10:51 AM)
Notes: 362 snapshots taken, and 104 snapshots good
MASAR allows user to preview a saved data set to make sure the data set is exact what is desired. By default, MASAR flags a data set as not approved. User has to explicitly approve one data set as good.

## Slide 32: EPICS V4 based Middle Layer Service
Snapshots taken with time
  Events (by Jan 15 2014 10:51 AM) total taken: 525, approved: 246
  Regular snapshot per shift
Date | Snapshots taken | Snapshots Approved
2012-03-21 9:28 | 0 | 0
2012-03-29 10:32 | 30 | 8
2012-03-30 18:01 | 31 | 9
2012-04-24 20:02 | 144 | 41
2012-05-11 10:27 | 210 | 63
2012-05-24 14:25 | 279 | 79
2012-06-07 18:28 | 331 | 96
2012-06-14 16:13 | 338 | 98
2013-12-17 7:34 | 460 | 186
2013-12-20 16:01 | 488 | 212
2013-12-23 14:48 | 489 | 213
2013-12-26 18:40 | 493 | 217
2013-12-27 18:18 | 497 | 221
2013-12-30 13:54 | 498 | 222
2014-01-02 12:12 | 500 | 224
2014-01-14 2:29 | 519 | 240
2014-01-15 8:40 | 525 | 246
Notes: 362 snapshots taken, and 104 snapshots good
MASAR allows user to preview a saved data set to make sure the data set is exact what is desired. By default, MASAR flags a data set as not approved. User has to explicitly approve one data set as good.

## Slide 33: EPICS V4 based Middle Layer Service
Database size growing over time (by Jan 15 2014 10:51 AM)
Notes: The file size was taken during regular maintenance. Therefore, there might have more than one snapshot at each time point, or does not have anything.
2 significant size increases. Caused by 5 snapshots for power supply ramping table of booster ring. That configuration contains over 60 PVs for booster ring power supplies, and each PV is a waveform with over 10,000 points.

## Slide 34: RESTful based Middle Layer Services
CAS PVAS
Diag db
CAS PVAS
PS db
CAS PVAS
RF db
Physical Device
Physical Device
Physical Device
CAS PVAS
VA db
Physical Device
CAS
JMS Service
Tracy-III Simulation
MySQL/IRMIS
PVAS
HTTP/REST
Lattice/Model
Python
MySQL
PVAS
HTTP/REST
Channel Finder
Java
MySQL/IRMIS
PVAS
HTTP/REST
MUNICONV
Python
SQLite/IRMIS
EPICS V4
MASAR
Python
Ethernet
Distributed Front-Ends
MySQL
PVAS
HTTP/REST
Olog
Java

## Slide 35: RESTful based Middle Layer Services
Channel finder services
  Originally by Ralph Lange
  Channel name look-up service
  Support property (name-value pair)
  Support tags
  Automatically load EPICS Channels at IOC initialization
  Client support
    Python library
    CS-Studio
  J2EE service
  MySQL as RDB backend

## Slide 36: RESTful based Middle Layer Services
IOCs
Glassfish Web service
/cf-update
Web proxy
CSS
Scripts to - populate properties
NFS
update daemon
dependency
data flow
Channel finder

## Slide 37: RESTful based Middle Layer Services
Channel Name | V2:SR:C02-MG:G04A{HFCor:FM1} |  | V2:SR:C02-MG:G04A{VFCor:FM1} | 
 | Fld-I | Fld-SP | Fld-I | Fld-SP
handle | READBACK | SETPOINT | READBACK | SETPOINT
elemName | FXM1G4C02A |  | FYM1G4C02A | 
elemType | HFCOR |  | VFCOR | 
elemField | x |  | y | 
devName | FM1G4C02A |  |  | 
sEnd | 65.5222 |  |  | 
cell | C02 |  |  | 
girder | G4 |  |  | 
symmetry | A |  |  | 
length | 0.044 |  |  | 
ordinal | 263 |  | 264 | 
tags | eget | eput | eget | eput
 | x |  | y | 
 | sys.SR |  |  | 
Virtual accelerator property into channel finder
Notes: Value are generated from the property table when generating VA EPICS DB

## Slide 38: RESTful based Middle Layer Services
Olog
  Collaboration by NSLS II@BNL & FRIB@MSU
  Log an entry
    Time, owner, text, attachments, logbooks, tags, properties
  J2EE service
  MySQL as RDB backend
  Client support
    Python library
    CS-Studio
    Web interface

## Slide 39
pvManager
Graphene
IOC
CA client (JCA/CAJ)
CSS Core
ChannelFinder Integration
ChannelFinder
…
…
DataBrowser
BOY
IOC
…
IOC
pvA client
IOC
…
v3
v4
Publish/subscribe
Command/response
v4
Masar
...
pvA
Sim
Test
API
…
CA
Core Client Technologies
Data Sources
Aggregation
Visualization
vTypes
Data Definition
BEAST
Log Viewer
AccelUtils
Olog Integration
Olog
API
Logbook
…
pyOlog
…
Scripts and utilities
Web UI and other clients
Java/Python
Web based REST services
CS-Studio
Courtesy of Kunal Shroff
ChannelFinder Integration
ChannelFinder
API
Notes: To begin with this slides gives an overview of the various pieces that represent the architecture of our controls and high level physics applications, tools and services along and their relation ship with each other.
// maybe
Epics (both v3 and v4) is the control system we use
The core technologies provide the means to efficiently communicate with the Control system
CS-Studio is our primary user interface tool

## Slide 40: RESTful based Middle Layer Services
Olog web view

## Slide 41: RESTful based Middle Layer Services
Olog CS-Studio view

## Slide 42: RESTful based Middle Layer Services
Lattice and Model Service
Beam Parameter
Beam Parameter
Simulation/ Measurement
Beam Parameter
Lattice Deck
Beam Parameter
Lattice
(Geometric + Strength)
Model
(Simulation output)

## Slide 43: RESTful based Middle Layer Services
Lattice Model Service Architecture
Finished
User Apps
Planning
Developing
MySQL (Lattice: geo+strength, Model: TWISS, T-Matrix, Close Orbit, …)
Python Data API
Python-MySQLdb
V4 channelRPC service
Simulation
(Tracy-III & Elegant)
RESTful
Python Client
Scripting
CSS/BOY
Java Client
Others
(Matlab)
Browsers
RESTful
pvAccess
RESTful
pvAccess
pvAccess
Data Processing API
Django
HTML

## Slide 44: RESTful based Middle Layer Services
Service implemented under Django framework
  Provide REST service interface
    Currently, support RESTful GET & POST
  3 lattice deck acceptable
    Predefined tab-separated plain lattice
    Tracy-3
    Elegant
  2 simulation codes support by server
    Tracy-3 & elegant
  Client support
    Python library
    Web UI
  MySQL as RDB backend
  V4 implementation has been planned on top

## Slide 45: RESTful based Middle Layer Services
Lattice view

## Slide 46: RESTful based Middle Layer Services
Model view

## Slide 47: RESTful based Middle Layer Services
MUNICONV Service
  Multiple unit conversion
    First implementation targeting on magnets
    Convert value between different unit systems
      i: power supply current
      b: magnetic fields
      k: value in model/lattice domain
  RESTful service interface under Django
    Currently, support GET method
  MySQL as RDB backend
  Client support
    Python library
    Web UI
  V4 implementation has been planned on top

## Slide 48: RESTful based Middle Layer Services
MUNICONV Architecture
Finished
User Apps
Planning
Developing
MySQL (Lattice: geo+strength, Model: TWISS, T-Matrix, Close Orbit, …)
Python Data API
Python-MySQLdb
V4 channelRPC service
RESTful
Python Client
Scripting
CSS/BOY
Java Client
Others
(Matlab)
Browsers
RESTful
pvAccess
RESTful
pvAccess
pvAccess
Conversion functions
Django
V3 IOC
Conversion functions
HTML

## Slide 49: RESTful based Middle Layer Services
MUNICONV Data stored in RDB
  Capture interested raw data
    Measurement data, fitting parameters, fitting algorithm
    Serial #, device name, installation info
    Component type
  Measurement data
    For each individual magnet
    For magnet type

## Slide 50: RESTful based Middle Layer Services
MUNICONV Capability
  Convert value between predefine unit system
  Unit is determined usually by magnet measurement
  Conversion algorithm plugable
MUNICONV Support magnets
  Standalone function magnet
  Function combined magnet
    A skew quadrupole with H&V correctors for example
  Serial powered magnet chain

## Slide 51: RESTful based Middle Layer Services
{'i2b': {'auxInfo': 1,
'function': '',
'algorithmId': 1,
'initialUnit': '',
'resultUnit': ''},
'b2i': {'auxInfo': 1,
'function': '',
'algorithmId': 1,
'initialUnit': '',
'resultUnit': ''},
'b2k': {'auxInfo': 2,
'function': '',
'algorithmId': 0,
'initialUnit': '',
'resultUnit': ''},
…
}
# auxInfo: an additional information,
# could be used for example the fitting order
# of polynomial fitting,
# 0: not use; 1: linear fit; 2: 2nd order poly fit; ...
# or the order of fitting result, for example
# 1: kick angle, rad/degree;
# 2: K1, 1/m2;
# 3: K2, 1/m3;
# 4: K3, 1/m4; ...
# algorithmId: id to show which algorithm to use,
# 0: linear fitting with given function
# 1: high order polynomial fitting with given function
# 2: polynomial fitting using raw data
# 3: interpolating with raw magnetic data
# 4: …
Pluggable and extendable conversion algorithm

## Slide 52: RESTful based Middle Layer Services
MUNICONV WEB View

## Slide 53: RESTful based Middle Layer Services
IDOD service for insertion device
  Data service to store both online data and offline data
  Same architecture to be implemented using django
  Under active development, and should be released soon
Data service for beam based fast interlock
  Provide a data warehouse
  Keep all history data
  Under design

## Slide 54: Middle Layer Services Integration
Channel Finder
MUNICONV
MASAR
Lattice/Model
Other Service
(IDOD)
Client App
IOCs
(PVs in Phyisics Unit)
IOC

## Slide 55: Beam Commissioning
MySQL
PVAS
HTTP/REST
…
…
High Level Applications
Distributed Front-Ends
CAS PVAS
Diag db
CAS PVAS
PS db
CAS PVAS
RF db
Physical Device
Physical Device
Physical Device
CAS PVAS
VA db
Physical Device
CAS
JMS Service
Tracy-III Simulation
MySQL/IRMIS
PVAS
HTTP/REST
Lattice/Model
Python
MySQL
PVAS
HTTP/REST
Channel Finder
Java
MySQL/IRMIS
PVAS
HTTP/REST
MUNICONV
Python
SQLite/IRMIS
EPICS V4
MASAR
Python
Ethernet
Python Apps
CAC PVAC REST
MMLT
CAC PVAC REST
Matlab Apps
CAC PVAC REST
Channel Arch
CAC PVAC REST
CS-Studio
pvManager
CAC PVAC REST
MySQL
PVAS
HTTP/REST
Olog
Java

## Slide 56: Beam Commissioning
2013-11-27: restart beam commissioning
2013-11-29: accelerate to 200 MeV in single

## Slide 57: Beam Commissioning
2013-11-27: restart beam commissioning
2013-11-29: accelerate to 200 MeV in single
2013-12-07: injection into booster
2013-12-10: beam spinned the Booster Ring
Notes: December 2, 2013: 24 hour commissioning starts.
December 5, 2013: Fault studies authorized and completed.
December 6, 2013: Fault study interim report approved. Injection into booster authorized.

## Slide 58: Beam Commissioning
2013-11-27: restart beam commissioning
2013-11-29: accelerate to 200 MeV in single
2013-12-07: injection into booster
2013-12-10: beam spinned the Booster Ring
2013-12-16: beam circulated tens of thousand turns in the booster ring

## Slide 59: Beam Commissioning
2013-11-27: restart beam commissioning
2013-11-29: accelerate to 200 MeV in single
2013-12-07: injection into booster
2013-12-10: beam spinned the Booster Ring
2013-12-16: beam circulated tens of thousand turns in the booster ring
2013-12-21: beam captured by the booster RF

## Slide 60: Beam Commissioning
2013-11-27: restart beam commissioning
2013-11-29: accelerate to 200 MeV in single
2013-12-07: injection into booster
2013-12-10: beam spinned the Booster Ring
2013-12-16: beam circulated tens of thousand turns in the booster ring
2013-12-21: beam captured by the booster RF
2013-12-31: beam boosted to 3 GeV (1.5 mA out 3 mA )

## Slide 61: NSLS II Construction
Oct 2009

## Slide 62: NSLS II Construction
Oct 2010

## Slide 63: NSLS II Construction
Oct 2011

## Slide 64: NSLS II Construction
Jul 2013
Linac
Booster
Storage Ring
Control Room
Controls Group

## Slide 65: Conclusion
Overviewed NSLS II project
Virtual accelerator provided solid support
2 technologies for middle services
  V4 service, and RESTful web services
  Satisfy various requirement
  Play critical role during commissioning
Support beam commissioning well
  Beam to 3GeV on 2013-12-31